## Slide 1: Step 1: Rainwater collected on the terrace and flows through the strain
Strain
Terrace Area: 630 Square feet

## Slide 2: Step 2: Water collected in the tank of 1000 liter capacity.
1000 liter tank

## Slide 3: Step 3: Collected water sediments few seconds and overflows in another 500 liter capacity tank.
Overflow water

## Slide 4: Step 4: Overflowed water from 1000 liter tank collected in 500 liter tank.
500 liter tank
1000 liter tank to collect water from separate 150 square feet area blue fiber roof.

## Slide 5: Step 5: Water further sediments in 500 liter tank for few seconds and overflowed through one inch pipe

## Slide 6: Step 6: If water not sufficient for overflow, the gear valve is used after sufficient sedimentation time.
Gear Valve

## Slide 7: Step 7: Another gear valve used for separate tank of 1000 liter.
Gear valve

## Slide 8: Step 8: Water from both 500 liter and 1000 liter tanks flows down towards ground.
rain water flows towards ground

## Slide 9: Step 9: Water flowing down continued

## Slide 10: Step 10: Rainwater harvested and recharged in the ground
28 feet deep boring with 10 feet filter pipe.
rain water flowing towards ground

## Slide 11
Finally, If you are interested, please try to visit my home at Sankhamul, Kathmandu, ward number 10 and observe the rain water harvesting system.
Thank you very much.
Date: 21st April 2015
Kaji Awaley
kaji.awaley@gmail.com
Technicians working for ground water recharge by rain water harvesting